## Slide 1: Design and Implementation of a 4-Bit RISC CPU Datapath
VERILOG HDL · 4-BIT RISC · 3-STAGE PIPELINE
Name: Than Nguyen Minh Nguyen
Roll no: SE204340

## Slide 2: Project Aim and Scope
PROJECT AIM
To design, implement, and verify a functional 4-bit RISC CPU using Verilog HDL.
PROJECT SCOPE
Datapath Design
ALU, register file, and memory units.
Control Design
Instruction decoder and hardwired control.
Pipeline Architecture
Three stages — IF, ID, and EX.
Functional Verification
Simulation and testbench-based testing.
Expected Outcome: A working CPU capable of executing arithmetic, logic, memory, and jump instructions.
4-Bit RISC CPU Datapath · 02 / 10

## Slide 3: System Specifications
Parameter | Specification
CPU architecture | 4-bit RISC-style
Instruction width | 12 bits
General-purpose registers | 4 registers: R0–R3
Instruction memory | 16 × 12 bits
Data memory | 16 × 4 bits
Program counter | 4 bits
Pipeline stages | IF, ID, EX
Control mechanism | Hardwired control
Implementation language | Verilog HDL
4-Bit RISC CPU Datapath · 03 / 10

## Slide 4: Instruction Set Architecture
INSTRUCTION FORMAT · 12 BITS
[11:8]
Opcode
Selects the operation
[7:6]
Rd
Destination and first source
[5:4]
Rs
source register
[3:0]
Immediate / Address
Constant or address
SUPPORTED INSTRUCTIONS
Arithmetic
ADD · SUB
Logic
AND · OR · XOR · NOT
Data transfer
LDI · MOV
Memory access
LOAD · STORE
Control flow
JMP · JZ
Total: 12 implemented instructions, with 4 reserved opcodes.
4-Bit RISC CPU Datapath · 04 / 10

## Slide 5: Overall CPU Datapath
MAIN FUNCTIONAL BLOCKS
Program Counter (PC)
Instruction Memory
IF/ID and ID/EX Pipeline Registers
Instruction Decoder
Register File
Operand Multiplexer
Arithmetic Logic Unit (ALU)
Flag Register
Data Memory
Write-Back Multiplexer
Branch Unit
MAIN DATA FLOW
Instruction Memory
↓
Decoder
↓
Register File / ALU
↓
Write-Back
MEMORY ORGANIZATION
Separate instruction and data memories (Harvard model).
4-Bit RISC CPU Datapath · 05 / 10

## Slide 6: Three-Stage Instruction Pipeline
IF
Instruction Fetch
Read the instruction using the PC.
Prepare the instruction for decoding.
ID
Instruction Decode
Identify the opcode and instruction fields.
Generate control signals.
EX
Execute
Read operands and execute the operation.
Access data memory when necessary.
Write results and update applicable flags.
KEY BENEFIT
Multiple instructions occupy different stages simultaneously.
PERFORMANCE
One completed instruction per clock after pipeline fill.
4-Bit RISC CPU Datapath · 06 / 10

## Slide 7: Pipeline Registers and Hazards
PIPELINE REGISTERS
IF/ID
Stores the fetched instruction, its address, and a valid bit.
ID/EX
Stores decoded control signals, register fields, immediate data, address, and a valid bit.
HAZARD MANAGEMENT
Hazard | Design approach
Structural | Separate instruction and data memories
Data | Read operands during EX after preceding write-back
Control | Flush two younger instructions after a taken jump
2
Jump penalty: 2 clock cycles. A flushed pipeline slot behaves as a NOP.
4-Bit RISC CPU Datapath · 07 / 10

## Slide 8: Hardwired Control and Branching
ID STAGE
Instruction decoder
Decodes the opcode.
Generates ALU, register, memory, and flag control signals.
Uses safe default values for reserved opcodes.
EX STAGE
Branch unit
JMP addr
always changes the PC.
JZ addr
jumps only when Zero = 1.
BRANCH CONTROL
Control signals
pc_sel = 1
select the jump target.
flush = 1
clear the two younger pipeline instructions.
Reserved opcodes: Behave as NOPs.
4-Bit RISC CPU Datapath · 09 / 10

## Slide 10: Verification Strategy
88
total checks across four testbenches
Testbench | Checks
ALU | 11
Register file | 11
Control unit | 22
Complete CPU | 44
Total | 88
VERIFICATION COVERAGE
Arithmetic and logic results.
Register reads, writes, and reset.
Instruction decoding and control signals.
Sequential program execution.
JMP and conditional JZ behavior.
Pipeline flushing and valid reset state.
Checks for unknown x values on key outputs.
4-Bit RISC CPU Datapath · 10 / 10